## Slide 1: Module 6: Code Reusability: Libraries, Packages and Subprograms in VHDL
OHIO UNIVERSITY – SCHOOL OF EECS – EE5143 – DIGITAL DESIGN WITH VHDL AND VSLI

## Slide 2
Code reusability
General ideas
Although each VHDL program is unique as it relates to the description of a particular digital system, it is often the case that some parts of it can be similar in structure so that they are repeated in various parts of the overall program. It is then beneficial to identify such repeating blocks of code for increased efficiency of program execution. This is done by describing such recurring pieces of code only once and using a suitable means to invoke them whenever needed.
This is essentially the idea behind subprograms. Most high level languages support such recurring code definitions. The mechanisms provided to handle code reusability within a program are through constructs called ‘procedures’ and ‘functions’. Both of them are pieces of once-defined reusable code that can be used anywhere in the program without explicitly writing the procedure or function code.

## Slide 3
Code reusability
General ideas
VHDL supports both procedures and functions. Procedures are invoked (activated) by explicitly calling them by their label (name) whereas functions are invoked by using their names within a valid expression.
Packages and libraries are used to declare and store components (often for ‘structural’ type VHDL programming). These are also used for storing type declarations, functions and procedures so that they can be used later in other programs.
Both libraries and packages can be either written by a programmer or supplied by a software or hardware vendor to be used in VHDL programs.
Standard libraries, such as IEEE VHDL libraries are universally used in almost all VHDL programs to provide standard definitions of signals, variables, data types etc.

## Slide 4
Libraries and packages in VHDL
VHDL libraries & packages
Packages are self-contained design units where reusable code for components, procedures or functions can be placed. Packages can then be compiled into a library. When the contents of a code unit contained in a package are needed, these can be easily called using the following steps.
An entire library can be made visible by using a library clause (placed at the beginning of the VHDL program, such as:
library ieee;
This clause makes the ieee library, for example, visible to the VHDL program that follows this clause. However, in order to actually be able to use the contents of the library, selected packages names must also be made visible using a separate ‘use’ clause such as:
Use library_name.package_name.item

## Slide 5
Libraries and Packages in VHDL
VHDL libraries & packages
Here library_name is the name of a VHDL library, package_name is the name of a package contained within this library and item is the name of a code unit contained within that package. This clause enables the code unit ‘item’ to become visible and usable within the following VHDL program.
A package consists of a package declaration and an (optional) package body. Within the declarative part there are only declarations of types, components, functions and procedures but not their full definitions. The full definitions appear in the package body which is needed whenever procedures and/or functions are contained in a package.
Either selected items contained within a package can be made visible, as in the example on the previous slide, or all individual code units contained within a package can be made visible by using the reserved word ‘all’, such as:
Use library_name.package_name.all

## Slide 6
Libraries and packages in VHDL
VHDL libraries and packages
A package is declared by starting with the VHDL reserved name ‘package’ then stating a user-defined package name followed by the reserved word ‘is’, such as:
package my_package is
After this, one or more components, procedures or functions can be declared, followed by the reserved word ‘end’ and the name of the package.
The actual definitions of the various package code units (components, procedures or functions) are contained in a package body that is started as:
package body my_package is
This is followed by the definition of all code units and ends with:
end my_package;

## Slide 7
Procedures in VHDL
VHDL procedures
By defining a procedure a piece of code is set aside to be used whenever needed by calling its procedure name. A procedure can compute one or more parameter and return it to the calling program. Procedures can have only sequential statements in them. While no new signals can be declared in procedures it is possible to declare variables and constants within a procedure body for local use within the procedure block.
Procedures and functions are declared and defined in the same way: either in the architecture’s declarative region or in a VHDL package.
It is a common practice to define one or more procedures in a package which is then placed in a reusable library.

## Slide 8
Functions in VHDL
VHDL functions
Unlike procedures, VHDL functions can only have parameters that have input mode and thus a functions formal calling parameters cannot be modified. Also, unlike procedures, functions can only return one argument. Just like procedures, functions can also have only sequential statements in them. While no new signals can be declared in functions it is possible to declare variables and constants within a function body for local use within the function block.
Both procedures and functions can be defined in the declarative region of an architecture, instead of placing them in a package. If this is done then the their definition also serves as their declaration and no separate declarations are needed. A procedure or function defined in the declarative part of an architecture body is only visible to that architecture. By putting them inside library packages the code can be more widely used with other programs as well.

## Slide 9
Functions in VHDL
VHDL functions
VHDL functions can be used for many purposes. Small algorithms can be coded as functions. Simple digital components can also be expressed as functions. Functions can also be used for overloading operators. This means that multiple functions can be written to service a single operator each with different types of arguments. Then the particular function that matches the argument type in the function call is automatically used.
Many standard functions (and type definitions etc.) are contained in the IEEE standard 1076 library which is used with the following library and use clauses:
Library ieee;
Use ieee.std_logic_1164.all;